#### Part Numbers: 	00644-52501-***

00644-52502-***

*** Corresponds to the color code and can be found on the box label and in the chart to the right

Section I - Installation Preparation

# Kit Contents

| Item # | Quantity Reqd. | Description |
| --- | --- | --- |
| 1 | 1 | Front Fascia |
| 2 | 2 | Fog Light Grilles |
| 3 | 6 | Fog Light Grille Clips |
| 4 | 1 | Fog Light Kit |
| 5 | 1 | Alcohol Wipe |
| 6 | 1 | 3M Adhesion Promoter |

Hardware Bag Contents

| Item # | Quantity Reqd. | Description |
| --- | --- | --- |
| 1 | 8 | Screw |
| 2 | 6 | Plastic U-Nut (Black) |

Additional Items Required For Installation

| Item # | Quantity Reqd. | Description |
| --- | --- | --- |
| 1 |  | Cloth Rag |

Conflicts

Note:

Tools Required

| Safety Tools |  |
| --- | --- |
| Special Tools |  |
| Installation Tools |  |

Color Applicability/Trim Level

| Accessory Color |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Vehicle/Trim Color |  |  |  |  |  |  |  |  |  |  |
| Absolutely Red 3P0 |  |  |  |  |  |  |  |  |  |  |
| Auburn Sky Pearl 3N3 |  |  |  |  |  |  |  |  |  |  |
| Black 202 |  |  |  |  |  |  |  |  |  |  |
| Cibola Gold Metallic 585 |  |  |  |  |  |  |  |  |  |  |
| Crystal White 062 |  |  |  |  |  |  |  |  |  |  |
| Electric Green 6R4 |  |  |  |  |  |  |  |  |  |  |
| Diamond White Pearl 051 |  |  |  |  |  |  |  |  |  |  |
| Graphite Gray Pearl 1C6 |  |  |  |  |  |  |  |  |  |  |
| Imperial Jade Mica 6Q7 |  |  |  |  |  |  |  |  |  |  |
| Intensa Blue Pearl 8N8 |  |  |  |  |  |  |  |  |  |  |
| Millennium Silver 1C0 |  |  |  |  |  |  |  |  |  |  |
| Solar Yellow 576 |  |  |  |  |  |  |  |  |  |  |
| Spectra Blue 8M6 |  |  |  |  |  |  |  |  |  |  |

General Applicability

Recommended Sequence of Application

| Item # | Accessory |  |
| --- | --- | --- |



# Legend

Section II - Installation Procedure

# PREPARATION

- It is strongly recommended that you pre-fit all parts to the car. This will ensure a proper fit when installing parts permanently.

###### Installation time is approximately 1 hour

### Setting Up the Vehicle

  - Raise the vehicle on a hoist.

  - Remove the front wheels.

### Removal Procedure

  - Unplug the turn signals and fog lights.

  - Remove the 4 clips that secure the radiator grille (Figure 1).  Retain them, as they will be reused later.

  - Remove the grille and set it aside.  It will be reused unless you have purchased the optional grille.

  - Remove the 8 factory screws from under the bumper cover (Figure 2).

  - Remove the center 6 (all but the outer 2) factory white U-Nuts and replace them with the L-Tuned supplied Black U-Nuts.

  - Remove the lower clip that retains the inner fender liner from each side of the vehicle.  They are located in the front of the front wheel wells (Figure 3). Retain them, as they will be replaced.

  - Remove the 2 screws that secure the bumper cover (Figure 4).  Retain them, as they will be reused later.

  - Remove the factory bumper cover.

  - Remove the turn signals (Figure 5).  Retain them, as they will be reused in the L-Tuned bumper cover.

### Installation Procedure

# Fog Light Kit Contents (Figure 6)

| Item # | Quantity Reqd. | Description |
| --- | --- | --- |
| 1 | 1 | Fog Light Assembly (Right) |
| 2 | 1 | Fog Light Assembly (Left) |
| 3 | 2 | Bracket A |
| 4 | 2 | Bracket B |
| 5 | 2 | Connector Housing |
| 6 | 8 | Screw |
| 7 | 8 | Tapping Screw |
| 8 | 8 | Washer |
| 9 | 2 | Foam Wrap |
| 10 | 2 | Tie Wrap |

  - Put the 2 lower grille pieces in place by attaching the 3 clips to the 3 tabs at each opening.

  - Use the small screws (Item 6) to attach the brackets to the lights (Figures 7 and 8).

  - Attach the lights to the backside of the L-Tuned Front Fascia using the tap screws (Item 7) and washers (Figure 9).

  - Remove the Lock from the Terminal Connector on the stock wire harness (Figure 10).  Note that there are 2 types.  If you have Type A, you will need to remove a lock from both ends of the connector (Figure 11).

  - Remove the Terminal from the Connector Housing.  Use a small screwdriver to release the tab and remove the wire as shown in Figure 12.

  - Remove the Rear Holder from the L-Tuned Supplied Connector Housing (Item 5, Figure 13).

  - Place the Terminals through the L-Tuned Supplied Rear Holder and into the Connector Housing (Figure 14).

  - Plug the L-Tuned Supplied Light into the factory wire harness (now with L-Tuned Connector attached).  Wrap with the supplied Foam (Figure 15).

  - Use the L-Tuned supplied Tie Wraps to collect any excess harness (Figure 16).

  - Mount the factory turn signals into the L-Tuned bumper cover (Figure 17 and refer to Figure 5).

  - Put the L-Tuned bumper cover in place.

  - Replace the 2 screws removed in Step 6 of the Removal Procedure (Refer to Figure 4).

  - Replace the 2 clips removed in Step 5 of the Removal Procedure (Refer to Figure 3).

  - Use the 8 L-Tuned-supplied screws to secure the bumper cover to the vehicle (Refer to Figure 2).

  - Install either the factory or the L-Tuned radiator grille (Refer to Figure 1).

  - Plug in the turn signals and optional fog lights.

  - Replace the front wheels.

Section III - Functional Verifications

Check:

Clean the areas where the parts are being installed

Pre-fit and mark out the position of the new parts

Make sure all the parts are securely attached to the car body

Look For:

Check for gaps or separations between the parts and the vehicle body

# Text boxes

STOP

STOP: Damage to the vehicle may occur.  Do not proceed until process has been complied with.

OPERATOR SAFETY: Use caution to avoid risk of injury

CRITICAL PROCESS: Proceed with caution to ensure a quality installation.  These points will be audited on a completed vehicle installation

GENERAL PROCESS: This highlights specific processes to ensure a quality installation.  These points will be audited during the accessory installation

TOOLS & EQUIPMENT: This calls out the specific tools and equipment required for this process

# Figure 9

Tapping Screw

# Figure 6

# Figure 3

# Figure 17

Brown 2-Terminal

Connector

Remove (8)

Top

Screw (2)

STOP

Light 00036

# Figure 5

Screw (2)

Type A

Lock

Brown 2-Terminal

Connector

Washer

Up

# Figure 4

Front View

Screw (2)

Bottom

Bracket B

# Figure 1

Bracket A

# Figure 7

Light 00038

# Figure 8

Screw (2)

Bracket B

Bracket A

# Figure 2

###### Body Kit Terminology

Lock

Type B

# Figure 10

# Figure 12

Brown 2-Terminal

Connector

Screwdriver

Lock

# Figure 11

Terminal

Connector Housing

Wire

Lock

Screwdriver

Rear Holder

Rear Holder

White/Black

L-Tuned  Supplied

Connector Housing

# Figure 16

Red/Yellow

# Figure 14

Terminal

# Figure 13

Factory Harness

Foam Wrap

Fog Lamp Harness

# Figure 15

Center of Connector

Top

View