#### Part Numbers: 	00644-52501-***

00644-52502-***

*** Corresponds to the color code and can be found on the box label and in the chart to the right

Section I - Installation Preparation

# Kit Contents

| Item # | Quantity Reqd. | Description |
| --- | --- | --- |
| 1 | 1 | Rear Valance |
| 2 | 1 | Alcohol Wipe |
| 3 | 1 | 3M Adhesion Promoter |

Hardware Bag Contents

| Item # | Quantity Reqd. | Description |
| --- | --- | --- |
| 1 | 4 | Press Fasteners |

Additional Items Required For Installation

| Item # | Quantity Reqd. | Description |
| --- | --- | --- |
| 1 |  | Cloth Rag |
| 2 |  | Prep Solvent 70 |

Conflicts

Note:

Tools Required

| Safety Tools |  |
| --- | --- |
| Special Tools |  |
| Installation Tools |  |
| Grease Pencil or Masking Tape and Tape Measure |  |

Color Applicability/Trim Level

| Accessory Color |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Vehicle/Trim Color |  |  |  |  |  |  |  |  |  |  |
| Absolutely Red 3P0 |  |  |  |  |  |  |  |  |  |  |
| Auburn Sky Pearl 3N3 |  |  |  |  |  |  |  |  |  |  |
| Black 202 |  |  |  |  |  |  |  |  |  |  |
| Cibola Gold Metallic 585 |  |  |  |  |  |  |  |  |  |  |
| Crystal White 062 |  |  |  |  |  |  |  |  |  |  |
| Electric Green 6R4 |  |  |  |  |  |  |  |  |  |  |
| Diamond White Pearl 051 |  |  |  |  |  |  |  |  |  |  |
| Graphite Gray Pearl 1C6 |  |  |  |  |  |  |  |  |  |  |
| Imperial Jade Mica 6Q7 |  |  |  |  |  |  |  |  |  |  |
| Intensa Blue Pearl 8N8 |  |  |  |  |  |  |  |  |  |  |
| Millennium Silver 1C0 |  |  |  |  |  |  |  |  |  |  |
| Solar Yellow 576 |  |  |  |  |  |  |  |  |  |  |
| Spectra Blue 8M6 |  |  |  |  |  |  |  |  |  |  |

General Applicability

Recommended Sequence of Application

| Item # | Accessory |  |
| --- | --- | --- |



# Legend

Section II - Installation Procedure

# PREPARATION

- It is strongly recommended that you pre-fit all parts to the car and mark the top outline with a grease pencil or masking tape before removing tape backing on the part. This will ensure a proper fit when installing parts permanently.

- Once the parts are installed for the first time onto the car body, removing them because they are not aligned will degrade the adhesive tape. If the parts are installed twice with the same adhesive tape, they may come unattached from the vehicle after it has been driven for some time. If parts have to be installed twice, you must use new 3M thick acrylic foam tape.  Call L-Tuned for additional tape if necessary.

- Part installation onto the correct spot on the vehicle is also very important. Parts that are misaligned by as little as ½” may not seat firmly to the body. This happens because the vehicle body changes lines and angles when you move away from the designated L-Tuned adhesion point.

- Parts need to be firmly pushed onto the vehicle to ensure proper adhesion. The tape needs a firm amount of pressure to correctly adhere to the car body. Use your fingers and the palms of your hands to firmly push the urethane part on the areas directly above the tape. This pressure is very important to “seat” the part onto the body.

### Setting Up the Vehicle

  - Raise the vehicle on a hoist.

  - Remove the rear wheels.

### Installation procedure

  - Remove the 2 factory screws (1 from each side) from the back of the rear wheel well (Refer to Figure 4).  Retain them, as they will be used later.

  - Remove the 4 factory press fasteners from the underside of the rear bumper cover (Figure 1).

  - Test fit the L-Tuned part by securing it with the factory screws removed in Step 1 and at least 2 L-Tuned-supplied press fasteners.  Mark the outline of the part with a grease pencil or masking tape (Figure 2).

  - Remove the part and clean the area where the valance will attach to the vehicle with Prep Solvent 70 followed by alcohol.

  - Apply adhesion promoter to the area where adhesive will come in contact with the car.

NOTE: Make sure that the adhesion promoter does not go above the grease pencil line, as it will leave a film that is very difficult to remove.

  - In the center of the part, make a cut in the tape backing and pull a few inches off of the adhesive strip leaving “pigtails” (Figure 3).

  - Put the part in place (this is easier with 2 people).  Make sure to line it up with your grease pencil marks from Step 3, as it will be difficult to remove the adhesive after it has been placed.

  - Secure the part by pressing all 4 L-Tuned-supplied clips into holes the factory clips were removed from (Refer to Figure 1).

  - Pull a few inches of the adhesive backing and press the part firmly against the bumper to ensure a good bond.  Repeat until you have moved the entire length of the valance by working around the corners toward the wheel wells.

  - Secure the valance with the factory screws removed in Step 1 (Figure 4). Do not use air tools, as they will strip the threads.

  - Press the part firmly against the factory bumper cover to ensure a good bond.

  - Replace the rear wheels.

Section III - Functional Verifications

Check:

Clean the areas where the parts are being installed

Pre-fit and mark out the position of the new parts

Apply adhesion promoter before installing parts

Make sure all the parts are securely attached to the car body

Look For:

Look for grease pencil marks

Check for gaps or separations between the parts and the vehicle body

# Text boxes

STOP

STOP: Damage to the vehicle may occur.  Do not proceed until process has been complied with.

OPERATOR SAFETY: Use caution to avoid risk of injury

CRITICAL PROCESS: Proceed with caution to ensure a quality installation.  These points will be audited on a completed vehicle installation

GENERAL PROCESS: This highlights specific processes to ensure a quality installation.  These points will be audited during the accessory installation

TOOLS & EQUIPMENT: This calls out the specific tools and equipment required for this process

# Figure 4

# Figure 2

STOP

# Figure 3

CAUTION

- Parts need to be firmly pushed onto the vehicle to insure proper adhesion.

- Parts should be installed with car body temperature of 70oF or above.

- If temperature is below 70oF,you should use a heat gun to warm the vehicle and parts.

- You must clean all surfaces of the car where parts will come in contact, with Prep Solvent 70 followed by alcohol (supplied).

- You must apply the supplied adhesion promoter to all areas where the tape will come into contact with the car.

FAILURE TO FOLLOW THESE GUIDELINES MAY CAUSE ADHESION PROBLEMS

###### Installation time is approximately 1 hour

# Figure 1

###### Body Kit Terminology