## Slide 1: MANAGEMENT OF MEDICAL WASTE

## Slide 2: INTRODUCTION
The greater part of waste generated by health institutions is not hazardous and can be managed like household waste.
This constitutes about 75% to 90% of all waste generated in health institutions. However, the remaining10% to 25 % is hazardous and requires special arrangements for management

## Slide 3
Medical Waste means any solid and/or liquid waste including its container and any intermediate product, which is generated during the diagnosis, treatment or immunization of human beings or animals or in research or in the production or testing.

## Slide 4
Examples of hazardous health care waste are pathological waste such as tissues and body fluid, pharmaceuticals e.g. expired or unused drugs, sharps (syringes, disposable scalpels, blades, etc.), non sharps (swabs, bandages, disposable medical devices, etc) and chemicals (solvents, disinfectants, etc.), as well as waste water including effluents from mortuaries.
These pose risks by being infectious, toxic, radioactive or causing injuries.

## Slide 5
All health institutions and their officers have a duty of care to:
store waste correctly and prevent its spillage or loss of any kind;
Segregate wastes that require different methods of disposal;
Label waste to identify its source and contents;
Pass waste on only to persons authorized to receive it;
Receive waste only when properly authorised to do so and only from an authorised person;
Describe the waste (on the appropriate forms) in sufficient detail that subsequent carers and disposers can deal with it safely and are liable for any negligence on the part of the institution or its officers

## Slide 6: CLASSIFICATION OF HEALTH CARE WASTE
Generally, between 75-90% of the waste produced by health-care providers is non-risk or “general” health-care waste, comparable to domestic waste.
The remaining 10-25% of health care waste is regarded as hazardous.

## Slide 7
Broad categories of health care waste are:
1. General waste : not contaminated with blood, body fluids, or other harmful agents or materials (also referred to as domestic or municipal wastes) such as paper, fabrics, glass, food residues and containers.
2. Infectious waste: These are contaminated with blood, body fluids or can be infectious to patients, health care workers and the public.

## Slide 8
3. Hazardous waste: due to their potential for creating a variety of health risks as a result of their actual or presumed biological, chemical and/or radioactive contamination. Due to their potentially hazardous nature, these wastes require care from the point of generation until final disposal.

## Slide 9
TYPE | CLASSIFICATION AND DESCRIPTION | CONTENT/EXAMPLE
A | GENERAL/NORMAL WASTE This type of hospital waste is similar to domestic waste. It is not harmful except for the fact that it is produced within the hospital environment and therefore requires special handling. It includes sweepings from lawns, corridors, offices, workshop, stores, waste from kitchen, etc | Paper, cardboard, plastic materials including those from points of generation, kitchen waste, ash, sawdust, pieces of wood etc.

## Slide 10
TYPE | CLASSIFICATION AND DESCRIPTION | CONTENT/EXAMPLE
B | INFECTIOUS WASTE These types of waste from the hospital have physical and chemical characteristics similar to those of industrial hazardous waste and waste generated by both in-patients/outpatients or animals which is likely to contain pathogenic micro-organisms. It includes materials that can be infectious to patients, health care workers and the public. It therefore requires special management both inside and outside the hospital until it is finally disposed of. This may further be classified under the following sub classification: | Laboratory waste generated by microbiological investigation. Potentially infected blood and human and animal tissue. (e.g. HIV)

## Slide 11
TYPE | CLASSIFICATION AND DESCRIPTION | EXAMPLE
B1 | SHARPS These are sharp-edged wastes with puncture and/or cutting properties that pose risk of injury and infection. They may be stained or contaminated with blood or body fluids from injection rooms, surgical equipment etc | Needles, syringes, surgical blades, scalpels, test tubes, ampoules, glass instruments, pipettes etc
B2 | PATIENT WASTE/ CULTURE/ SPECIMEN These are wastes generated from in- or out-patient activities and may be contaminated or stained with blood or body fluids from surgical operations, injection room (other than sharps) etc. Clinical specimen, laboratory culture and human tissue. | Stained or contaminated material (e.g. soiled cotton wool, used bandages/dressings, gloves, linen, blood transfusion bags, urine, faeces). Culture plus specimen (e.g tissue culture, urine, stool)

## Slide 12
TYPE | CLASSIFICATION AND DESCRIPTION | EXAMPLE
B3 | PATHOLOGICAL/ORGANIC HUMAN/ANIMAL TISSUE This type of waste includes amputations and other body tissues resulting from surgical operations, autopsy (post-mortem), and birth and requires special treatment for ethical and aesthetic reasons | Internal body organs, amputated limbs, placentas foetus. Human liquid wastes (e.g. urine, blood products/blood) Effluents from mortuaries

## Slide 13
TYPE | CLASSIFICATION AND DESCRIPTION | EXAMPLES
C | TOXIC WASTE | 
C1 | PHARMACEUTICAL WASTE These are wastes generated from the pharmacy | Expired drugs (solid/liquid, plastic or glass containers) Residues of drugs in chemotherapy that may be cytotoxic, genotoxic, mutagenic or carcinogenic
C2 | CHEMICAL WASTE This is basically made up of spent chemicals from research and analytical laboratories, and pharmaceutical companies. | Acid, Alkali, organic substances, solvents, and heavy metals.

## Slide 14
TYPE | CLASSIFICATION AND DESCRIPTION | EXAMPLES
C | TOXIC WASTE | 
C3 | RADIOACTIVE WASTE Any solid, liquid, or pathological waste contaminated with radioactive isotopes of any kind. | Liquid-patient excreta, rest of solution administered to patient, gastric content.
C4 | RADIOLOGICAL WASTE Any waste material (solid or liquid) produced from image processing at the radiology department | Photographic developer Fixer solution X-ray photographic film

## Slide 15: WASTE SEGREGATION
This refers to the separation of the entire waste generated in a health facility in defined, different waste groups according to the specific treatment and disposal requirements
Segregation should be at source; that is it should take place as close as possible to the point of generation of the waste and should always be the responsibility of the waste producer

## Slide 16
Instruction posters regarding the procedure for waste segregation should be pasted in all areas where segregation takes place and other vantage points

## Slide 17: COLOUR CODING OF SEGREGATED WASTE
Colour coding means to combine different waste groups with “similar” hazards in one
main group and to identify this main group in a fast and easy way by a fixed colour.

## Slide 18
Colour codes should be used for waste containers and plastic bags to facilitate efficient segregation of waste.
Colour coding for the plastic bags should always correspond or match with the waste containers

## Slide 19
The recommended colour coding scheme for Ghana (adapted from WHO) is as follows:
BLACK- General waste (e.g. kitchen waste, paper, cardboard, sweeping etc)

## Slide 20
YELLOW - Infectious waste (e.g. sharps, patient waste, human/animal tissue and cultures/specimens) with the biohazard label
- Radioactive waste with the radioactive symbol.

## Slide 21
BROWN- Hazardous waste (e.g. expired drugs, vaccines, chemicals etc). Where only small amounts of chemical wastes are generated, these may be added to the infectious waste.

## Slide 22
Waste should be: Correctly bagged in appropriate colour-coded bags; Double bagged where: − The exterior of the bag is contaminated − The original bag is split, damaged or leaking − Kept in a rigid-sided, fire-retardant holder or container with a foot-operated lid, and, so far as is reasonably practicable, out of the reach of children − Only filled to ¾ full at the end of the day − Securely sealed and labelled with coded tags at the point of use to identify their source
Waste should not be: − Decanted into other bags, regardless of volume − Contaminated on the outside

## Slide 23: STORAGE OF WASTE
Hazardous waste should be removed from point of generation as frequently as circumstances demand, and at least weekly. Between collections, waste should be:
Stored in correctly coded bags, with bags of each colour-code kept separate
Situated in a centrally designated area of adequate size related to the frequency of collection
Sited on a well-drained, impervious hard-standing floor, which is provided with wash-down facilities
Kept secure from unauthorised persons, entry by animals and free from infestations
Accessible to collection vehicles

## Slide 24: TREATMENT AND DISPOSAL
WASTE TYPE | TREATMENT | FINAL DISPOSAL
General waste (food, paper, packing materials) etc | Biodigestion, Composting, Incineration (controlled combustion), Recycling (cardboard, paper, Glass) | Landfill, protected pits
Infectious waste, Sharps | Incineration Chemical disinfection Waste autoclave | Landfill
Patients’ waste | Incineration | Landfill
Culture/specimen | Discontinuation by autoclaving /incineration | Landfill
Pathological /organic Human tissue | Incineration Approved Burial Grounds | Landfill

## Slide 25
WASTE TYPE | TREATMENT | FINAL DISPOSAL
Hazardous Waste Pharmaceutical tablets and capsules | Crushing | Landfill
Syrups and injectables | Crushing of Injectables. Syrups -Diluted and washed down the drains | Landfill
Cytotoxic drugs, Vaccines | Incineration at high temperature | Landfill
X-ray photographic film, fixer solution | Incineration at high temperature | Landfill
Radioactive waste | Compaction, storage decay Immobilization. Ghana Atomic Energy to be consulted | Specially designed landfill
Laboratory Waste | Dilute with large volumes of water(12x) -For those that are infectious, chemical disinfection and incineration | Sewage. Landfill

## Slide 26
Incinerators