## Slide 1
2007 Radiation Refresher Training
Elayna Mellas
Radiation Safety Officer
Environmental Health & Safety Manager
Clarkson University
Downtown Snell 155
Tel: 315-268-6640
emellas@clarkson.edu
This training course has been partially adapted
from slides provided by Steve Backurz, Radiation
Safety Officer of The University of New Hampshire

## Slide 2: The Basics: Definitions
Radioactivity: The spontaneous disintegration or decay of an unstable atom, resulting in the release of energy (radiation).
Radiation: Energy in the form of particles or waves
Radioactive material: Any material that is composed of (or contains) radioactive atoms.
Contamination: Radioactive material in an undesirable location -- where we don’t want it.
Activity: The number of disintegrations (decays) occurring per unit of time.
Half Life: The time it takes for an amount of radioactive material to lose half (50%) of its activity because of decay.

## Slide 3: The Particles
ALPHA PARTICLE (): A high energy particle emitted from the nucleus during the decay of an atom.
  Travel a few centimeters in air
  Stopped by a sheet of paper or layer of skin
  Not an external hazard; ingestion or inhalation concern
BETA PARTICLE (): A high energy particle emitted from the nucleus during the decay of an atom
  Travel 10 to 20 feet in air
  Stopped by a book
  Shielding high energy betas with lead can generate more radiation due to Bremsstrahlung x-rays
GAMMA RADIATION (): Electromagnetic radiation emitted from the nucleus during decay
  No mass, no charge
  Travel many feet in air




## Slide 4
Measuring Radioactivity
  CURIE: A unit of activity defined by the number of radioactive decays from a gram of radium
  1Curie (Ci) = 2.22 E12 disintegrations/minute (dpm)
  Sub-multiples of the Curie:
    millicurie 1 mCi = 2.22 E9 dpm
    microcurie 1 uCi = 2.22 E6 dpm
    nanocurie 1 nCi = 2,220 dpm
    picocurie 1 pCi = 2.2 dpm
  Typical activities at Clarkson are in the Ci to mCi range
  OTHER UNITS OF MEASURE:
    Disintegrations per minute (dpm)
    Disintegrations per second (dps)
    The SI unit for activity is the becquerel (Bq)
    1 Bq = 1 disintegration/second
    1 Curie (Ci) = 3.7 E10 Bq or 37 GBq
      1 millicurie = 37 MBq
      1 microcurie = 37 kBq

## Slide 6: Biological Effects
Acute Exposure
  Large Doses Received in a Short Time Period
    Accidents
    Nuclear War
    Cancer Therapy
  Short Term Effects (Acute Radiation Syndrome 150 to 350 rad Whole Body)
  Anorexia Nausea Erythema Fatigue
  Vomiting Hemorrhage
  Epilation Diarrhea Mortality
Effects of Acute Whole Body Exposure on Man
Absorbed Dose (rads) | Effect
10,000 | Death in a few hours
1,200 | Death within days
600 | Death within weeks
450 | LD 50/30
100 | Probable Recovery
50 | No observable effect
25 | Blood changes definite
5 | 1st blood changes observed

## Slide 7: Biological Effects
Chronic Exposure
  Doses Received over Long Periods
    Background Radiation Exposure
    Occupational Radiation Exposure
  50 rem acute vs 50 rem chronic
    acute: no time for cell repair
    chronic: time for cell repair
  Average US will receive 20 - 30 rem lifetime
  Long Term Effects
    Increased Risk of Cancer
    0.07% per rem lifetime exposure
    Normal Risk: 30% (cancer incidence)

## Slide 8
Background Exposure
Your exposure to radiation can never be zero because background radiation is always present
  Natural Sources (Radon), Cosmic, Terrestrial, Medical Diagnostic, Consumer Products, etc
Total US average dose equivalent = 360 mrem/year
Total exposure
Man-made sources
Radon
Internal 11%
Cosmic 8%
Terrestrial 6%
Man-Made 18%
55.0%
Medical X-Rays
Nuclear
Medicine 4%
Consumer
Products 3%
Other 1%
11
Annual Dose from Background Radiation

## Slide 9
Occupational Limits (Researchers)
  5 rem per year (total effective dose equivalent: TEDE)
  50 rem per year (any single organ)
  15 rem per year lens of the eye
  50 rem per year skin dose
Members of Public
  100 mrem per year
  No more than 2 mrem in any one hour in unrestricted areas from external sources
Declared Pregnant Females (Occupational)
  500 mrem/term (evenly distributed)
  Declaration is voluntary and must be submitted to RSO in writing (see form on website)
Standards for Rad Protection

## Slide 10
Clarkson Anticipated
Worker Radiation Exposure
Anticipated Exposures: Less than the minimum detectable dose for film badges (10 mrem/month) - essentially zero
Average annual background exposure for U.S. population = 360 mrem/year
State and Federal Exposure Limits = 5000 mrem/year

## Slide 11: Reducing Exposure
Your goal is to eliminate any unnecessary dose to yourself, coworkers, & the public!
A
L
A
R
A
L ow
A s
R easonably
A s
A chievable
Notes: Overarching, fundamental precept pervasive in regulations.
Applies to personnel, public exposures, environmental releases / discharges.
“Reasonably” also includes economic considerations, as part of feasibility.
It is NOT ENOUGH to just comply with the established dose limits,
or even DFCI’s internal administrative limits!
If you can reduce your dose or exposure further
through reasonable steps or measures, then YOU MUST DO SO!

## Slide 12
Practicing ALARA
Time: minimize the time that you are in contact with radioactive material to reduce exposure
Distance: keep your distance. If you double the distance the exposure rate drops by factor of 4
Shielding: place a barrier between you and the radioactive source
Source Reduction: order and use the smallest amount of radioactive materials as necessary
Protective clothing: protects against contamination only - keeps radioactive material off skin and clothes
Protect Yourself & Your Colleagues!
OPTIMIZE USE OF ALL PROTECTIVE
MECHANISMS TO MINIMIZE DOSE.

## Slide 13: Shielding Recommendations:
Betas (ex: 32P):
  Use material with low atomic number, such as:
    Plastic, lucite, acrylic
    Wood, paper, cardboard
Gammas (ex: 125I or 51Cr):
  Use material with high atomic number, such as:
    Lead, concrete, bricks, stainless steel, cast iron

## Slide 14: Extra Precautions
Tritium (3H) is a low energy beta emitter and cannot be detected with a survey meter.
  Must do swipes and use liquid scintillation counter
  With 3H, you must control contamination to prevent internal exposures.
    Because you can’t see it or detect it easily, it’s movement can be insidious.
    You have no “real time” check on the contamination status of your work area.
32P is a high energy beta emitter. Use lots of shielding!
  The eye is sensitive to beta radiation. Wear safety glasses when working with 32P.
Some forms of 125I used in research are volatile; they can easily change from a solid or liquid to a gas.
  For volatile forms of 125I, any iodine gas released is radioactive, and can be quickly inhaled.
  Must have a special hood for use of volatile forms of 125I
  ENSURE YOU ORDER THE BOUND VERSION OF 125I

## Slide 15: Protective Clothing
Can be a very effective means of preventing skin, eyes, & clothing from becoming contaminated
  Eyewear to prevent splashes and provide shielding for high energy beta emitters
  Lab Coat
  Gloves (may want double layer)
Closed toe footwear
It is much easier to remove contaminated clothing than to decontaminate your skin!

## Slide 16: General Rules of Radiation Safety
Wash your hands every time you change gloves.

## Slide 17
Avoid Ingesting Radioactive Material
Don’t bring hands or objects near your mouth during an experiment
Eating, drinking, smoking, applying cosmetics are strictly prohibited in rad labs
Never mouth pipette
Never store personal food items in refrigerators or freezers used for radioactive material or other hazardous material storage

## Slide 18
Avoid Inhaling
Radioactive Material
Make sure you have proper ventilation for your experiments
When using volatile materials such as Iodine-125 and some Sulfur-35 compounds, be sure to use a fume hood that has been inspected and certified for proper airflow

## Slide 19
Contamination Control
All contaminated items must be labeled with “radioactive” tape (this includes all equipment that is used with rad materials)
Watch out where you put your “hot” hands during an experiment
Monitor yourself and your work area frequently for radioactivity (gloves, hands, feet, etc.)
Use most sensitive scale on meter (X0.1 or X1)
Have meter out and handy
Make sure to wash your hands frequently and after finishing an experiment
  Don’t bring radioactive material to lunch or to your home!
Monitor your work area before and after an experiment

## Slide 20: Detecting Contamination
Survey Meters are portable instruments that can be used to detect most spots of contamination - except for 3H.
Wipe Testing must always be done for 3H and lower activities (100 µCi or less) of 35S and 14C.
Notes: Wipe testing is great for all radionuclides (isotopes); recommend use for any amount of S-35 or C-14.
MUST know how to use the appropriate instrument before working with rad materials!
Check the instrument for serviceability before each use!

## Slide 21: Detecting Common Isotopes
Sodium Iodide (NaI) Probe
Survey Meter
Geiger- Mueller (GM) Probe
3H | Liquid Scintillation Counter
14C | GM Probe with Survey Meter
32P | 
33P | 
35S | 
51Cr | GM or NaI Probe w/ Survey Meter
125I | NaI Probe w/ Survey Meter
Liquid Scintillation Counter
Notes: Detectors (probes) are interchangeable (‘swappable’) on the survey meter base unit.
Many different types available, but most DFCI labs use Ludlum model 3 survey meters,
Usually with the pancake probe G- detector.

## Slide 22: Survey Meter Operability
Check calibration date (not older than 12 months)
Batteries must be fresh / good
Background count rate
Detector/instrument must be responsive
Miscellaneous conditions…?
Each USER must verify that the survey instrument is in good working order before each use.
Notes: Battery retainer (cover plate) properly latching, secured?
Cable split, cut? Bare conductor anywhere? 900 Volts!
Scintillation detector: check for light leaks, cable/connector ‘shorts’. Etc.

## Slide 23: Survey Meter “Background” Levels
Each detector will have its own background level.
1st check the background level - use it as a baseline.
Observed:
Background:
Zero:
Any reading higher than the background level means the item is radioactive.
Remember that background is radiation coming from the environment, and it cannot be prevented or eliminated.
!
"gross"
"net"
Notes: No such thing as “zero” radioactivity or radiation.
Looking for ‘net’ increase in count rate as an indicator of contamination, or elevated radiation.
Meter reading will fluctuate across a range – the average or center of that range is “background”.
Each meter (or the detector) can have a different background;
elevated background may indicate contamination of the detector!
May be hard to see or detect a small net increase; use your judgement, but anything > 3 times background is CLEARLY an indication of radioactivity or contamination.

## Slide 24
Clarkson Radiation Protection Program specifies
  Monitor all work areas at least once a week
  Instrument surveys and/or wipe surveys should be done after each experiment or more often if needed
  Isotope storage area must be surveyed at least once per month if no work is in progress
  Must keep records of all required surveys for inspection by RSO and state inspectors
Using a form with map of your lab on it is strongly recommended to make documenting surveys easier
A good rule of thumb for determining if contamination is present is to look for 2X background
Surveys and Monitoring

## Slide 25: MONITORING WORK AREAS
Keep the meter with you at all times.
Take frequent breaks to monitor how well you are doing. You should frequently check:
  Your hands and gloves - do not touch the meter until you know they are clean!
  Check your face and clothes - lab coat, wrists, shoes.
  Frequently check your work areas - bench, items on bench, equipment.
  Always check the FLOOR and other items you may have touched throughout the day:
    Keyboards, pens, telephones, backs of chairs, etc.

## Slide 26
The more often you CHECK yourself and work areas, the quicker you will find any contamination.
REMEMBER --
Why is time important?
Exposure minimization
Tracking extent (area contaminated)
Form: dry vs. wet, porosity / permeability
Notes: Time is important: exposure minimization, tracking extent, ‘cleanability’ may get worse with time…

## Slide 27: AVOID “HOT TRASH”
As you generate waste, meter things before you throw them in the regular trash.
As part of your personal survey, check the regular lab trash containers to ensure proper waste disposal.
Notes: Check the entire container after disposing what you believe to be non-radioactive materials;
In total (summed together) there may be enough radioactivity to be detected, while
Individual pieces may not have been ‘hot’ enough to be detected.

## Slide 28
Contamination surveys must be documented
Record the following
  Date performed
  Areas surveyed (map is best)
  Results in dpm/100 cm2 or mR/hour as applicable
  Initials or name of surveyor
  Instrument used and date of calibration
  Action taken if contamination is found
  Be sure to document all post-spill clean up surveys very well!
Documenting Surveys

## Slide 29: Decay-In-Storage of Wastes
Only for isotopes with half-lives less than 100 days
Keep all isotopes separate
Must keep an inventory with amount of activity
Remove or obliterate all radioactive labels prior to disposal
Store in labeled receptacle with clear plastic liner
Hold for 10 half-lives
Survey with appropriate detector and confirm indistinguishable from background
Dispose of without regard to radioactivity

## Slide 30: Liquid Scintillation Waste
Use “environmentally friendly” cocktail (water soluble)
  If tolulene/xylene based media must be used, keep separate
Must keep an inventory with amount of activity
Keep LSC separate from other liquid wastes
Store vials in flats, and check with RSO regarding method of disposal
Do not mix these with cocktails containing other radioactive materials

## Slide 31: Liquid Waste Disposal
Readily soluble or readily dispersible biological materials in water may go down the drain if
  No other hazard is present
  The concentration does not exceed the allowable monthly average concentration
  The total amount of radioactivity does not exceed 50 Ci/day
  The sink has been approved by the RSO and is appropriately designated and labeled
Must keep an inventory with amount of activity

## Slide 32
When cleaning up a spill, place absorbent material around the edges of the spill and clean from the outside edges toward the center to avoid spreading
Place materials used to clean the spill into appropriate radioactive waste containers
Notify others in the lab of the spill to prevent inadvertent spread of contamination
After clean-up, monitor all work areas using survey meter or wipe surveys, as applicable
Survey your hands, feet, clothing and all other materials that may have come in contact with the spilled material
General Spill Procedure

## Slide 33
A minor spill is one that involves small quantities, low activities, low energy, or low hazard radioactive materials that are confined to a relatively small area
Most spills that could occur in the lab would be minor and should be cleaned up by lab personnel ASAP
Use the general spill clean-up procedure and common sense
You do not need to notify the RSO in the event of a minor spill
Minor Spills

## Slide 34
An intermediate spill is one that involves larger quantities of radioactive material spread over a larger area
Intermediate spills could also involve small amounts of more hazardous radioactive materials such as higher energy emitters or volatile compounds
A spill outside a restricted area may also be considered intermediate since controlling the area may be difficult
Use the general spill clean-up procedure and common sense
Intermediate Spills

## Slide 35
Wear gloves, lab coats, dosimetry, and other protective clothing
Confine the contamination
Prevent the spread of contamination
Use a survey instrument to check yourself for contamination before leaving the area
Pay special attention to hands and feet
Restrict access to the spill area
Inform others in the immediate area and post notice if necessary
Contact the RSO (x2391) to report the situation
Intermediate Spills (cont’d)

## Slide 36
Emergency Response
Fire in radioactive areas:
  Notify Fire Department and RSO, clear the area of people. Remove any seriously wounded persons. Keep your distance
Theft of radioactive materials:
  Notify RSO (info is posted on lab door)
  State notification required
Notify RSO if you suspect:
  Inhalation, ingestion or other intake of radioactive material
  Accidental release of radioactive material into the environment

## Slide 37: Ordering & Receipt of Radioactive Materials
Only RSO is authorized to order radioactive material
Use the Radionuclide Purchase Request Form
Complete form and fax to RSO at 268-4475
Be sure to state any special ordering instructions (preferred delivery date, fresh batch, etc.)
Packages are received by RSO, checked for contamination, logged in, and delivered to the lab on the same day as receipt

## Slide 38: Posting & Labeling Notices
Labels
  All containers (unless exempt) must be labeled
  With “Caution – Radioactive Material”
  Should include radionuclide, quantity, date,
  initials, radiation levels, etc.
Posting
  New York Notice to Employees form
  Caution Radioactive Materials or X-Rays

## Slide 39
Access Restriction
Required by License and NY Regulations
Security and Control of Radioactive Material
Restricted area
Controlled area
Unrestricted area
Unrestricted area
Unrestricted area

## Slide 40
Security
Licensed RAM must be secured against unauthorized removal at all times
Must maintain constant surveillance for any radioactive material outside a restricted area
Lock labs containing radioactive material if last one out - even if it’s “just for a minute”
Challenge all unknown individuals with “May I help you?”
OK to ask for ID
Report to supervisor if suspicious

## Slide 41
Employee Rights
and Responsibilities
Right to report any radiation protection problem to state without repercussions
Responsibility to comply with the Radiation Protection Program and the RSO's instructions pertaining to radiation protection
Right to request inspection
  in writing
  grounds for notice
  signed
Responsibility to cooperate with NY State inspectors during inspections and RSO during internal lab audits

## Slide 42
Acknowledgements
This training course has been adapted from
slides provided by Steve Backurz, Radiation
Safety Officer of The University of New
Hampshire and by Eric Andersen, Radiation Safety Officer at the Dana-Farber Cancer Institute.